## Slide 1
Incorporating Nutrient and Heat Flow into River and Watershed Modeling to Better Predict Ecological Response across Large Scales
Engineer Research and Development Center (ERDC)
U.S. Army Corps of Engineers (USACE)
Todd Steissberg
Isaac Mudge
Kelsey Walak
LimnoTech
Anthony Aufdenkampe
Sarah Jordan
Jason Rutyna
Xavier Nogueira
Billy Johnson
Next Generation Ecological Modeling Tools Seminar Series
February 14, 2024

## Slide 2: Motivation and Background
Todd

## Slide 3: Introduction: Nutrient Flow through Ecosystems
Nutrient flow through ecosystems has a profound impact on how species utilize resources across watershed scales.
  Primary production
  Species distribution and abundance
  Ecosystem productivity and stability
  Community composition and diversity
  Carbon sequestration
Notes: Photo 1: Yellowstone National Park, showing complexity of landscape, flow, and vegetation
Photo 2: Complex and meandering flow across a landscape

## Slide 4: Introduction: Nutrient Flow and Disturbances
Human-caused disturbances are disrupting nutrient cycling
This causes cascading effects on ecosystem health and functioning.
The most common issue is nutrient excess:
  Causes
    Agricultural runoff
    Urbanization (stormwater)
    Industrial discharge
  Effects
    Rapid algae growth
    Oxygen depletion
    Harmful toxins

## Slide 5: Introduction: Nutrient Flow and Invasive Species
Invasive species can take advantage of changes in nutrient dynamics
  Nutrient-rich watersheds promote invasive aquatic plants, outcompeting native species.
  Excess nutrients stimulate algal blooms, providing invasive species with abundant food sources.
  Disrupted trophic interactions due to nutrient imbalances favor invasive predators over native prey.
  Nutrient-enriched soils create favorable conditions for invasive plant colonization.
Notes: Photo 1: Invasive water hyacinth, Sacramento River
Photo 2: Purple loosestrife, an invasive plant species of wetlands. Photo credit: Scott Jackson

## Slide 6: Introduction: Simulation of Nutrient Flow at Watershed Scales
Nutrient flow through ecosystems was not being simulated across watershed scales using a flexible integrated modeling system.
This hindered our ability to:
  Assess ecosystem risk analysis
  Predict morbidity and mortality of key species
  Predict spatial distribution of species across landscapes in response to changing conditions
  Identify effective ecosystem restoration strategies and management interventions
  Design measures to control the spread of invasive species
Notes: Photo 1: Terraced stream restoration project
Photo 2: River restoration, Trent River Valley, England

## Slide 7: Introduction: Project Objective
Water Resources Models
Water Quality Models (Nutrients & Temperature)
Ecological Models
Develop an integrated ecohydrology modeling system that simulates heat and nutrient flow through ecosystems.

## Slide 8: ERDC Environmental Modeling Capabilities
Linking environmental models with existing water resources models streamlines workflows and reduces costs. These simulate runoff, rivers, and reservoir hydraulics and hydrology
Our team at USACE-ERDC has developed ClearWater (Corps Library for Environmental Analysis and Restoration of Watersheds).
ClearWater provides environmental simulation capabilities with a suite of packages that are designed to leverage existing water resources models.
  ClearWater modules simulate water quality constituent kinetics, and heat budget processes. Capabilities include:
    Nutrients: Nitrogen, phosphorus, carbon, dissolved oxygen, algae, etc.
    Temperature (heat budget)
    General Constituents
  ClearWater-Riverine computes transport (advection and diffusion) of heat and constituent mass using outputs from any 2D hydrologic or hydrodynamic model
  Data visualization capabilities
  Framework to couple multiple models
Legacy Fortran modules integrated with HEC-RAS and HEC-ResSim
New Python modules and were developed to support 2D river-floodplain modeling
Runoff
Reservoirs
Rivers
Notes: Water quality modeling capabilities have advanced significantly, particularly in streamlining workflows and reducing costs by linking water quality (WQ) capabilities with existing hydrologic or hydraulic (H&H) models. The U.S. Army Corps of Engineers (USACE) has been at the forefront of developing widely deployed models that simulate watershed runoff, river hydraulics, and reservoir operations. To further enhance these capabilities, the USACE-ERDC (Engineer Research and Development Center) team has developed a modular library of environmental modeling capabilities, including the standalone river WQ model called ClearWater-Riverine.
ClearWater (Corps Library for Environmental Analysis and Restoration of Watersheds) is specifically designed to integrate environmental simulation capabilities with existing H&H models. It offers a range of modules that encompass various aspects of water quality dynamics and vegetation simulation. These modules simulate:
1. Nutrients – simulates the transport and transformation of nutrients within the river-reservoir system. They consider processes such as nutrient loading, uptake by algae, nutrient cycling, and water-column interactions.
2. Temperature – simulates heat budget dynamics, considering factors such as solar radiation, air temperature, and streamflow. It helps assess thermal impacts on water quality and aquatic ecosystems.
3. General Constituents - simulates a wide range of water quality constituents, such as dissolved oxygen, pH, turbidity, or specific pollutants. It enables the assessment of various water quality parameters relevant to specific modeling objectives.
4. Contaminants – simulates the fate and transport of contaminants, including pollutants or toxic substances. It aids in assessing the potential impacts of contaminants on water quality, ecological health, and human health.
5. Mercury – simulates the transport and fate of mercury in river-reservoir systems. It helps evaluate the fate and behavior of this toxic element and its potential impacts on water quality and ecosystems.
ClearWater includes a comprehensive water quality engine that computes the transport of heat and mass (including nutrients, contaminants, and other constituents) across the watershed. The model considers advection and diffusion processes, reflecting the movement and dispersion of pollutants or other water quality parameters.
Data visualization and reporting capabilities were developed to enable users to visualize and analyze water quality and environmental model results effectively. The integration of these capabilities into a comprehensive water quality framework ensures seamless interaction between the different modeling components, allowing for the development of comprehensive river-reservoir water quality models.
USACE-ERDC's ClearWater-Riverine model and the associated library of environmental modeling capabilities significantly enhance water quality modeling capabilities. By integrating water quality considerations into existing hydrologic and hydraulic models, these advancements support more comprehensive and efficient analysis of water resources, facilitating informed decision-making and effective management of river-reservoir systems.

## Slide 9: Water Quality and Environmental Systems Modeling
Water quality modeling tools:
  Watershed Runoff:
    GSSHA: Surface and sub-surface water quality modeling
    HEC-HMS: Surface runoff temperature modeling
  Reservoirs:
    CE-QUAL-W2: 2D reservoir-river hydrodynamics and water quality modeling
    HEC-ResSim: Reservoir operations and water quality modeling
  Rivers and Floodplains:
    HEC-RAS: 1D River hydraulics and water quality & vegetation modeling
    ClearWater-Riverine: 2D River-floodplain hydraulics and water quality modeling with HEC-RAS-2D
ERDC’s Corps Library for Environmental Analysis and Restoration of Watersheds (ClearWater) provides environmental simulation capabilities that leverage existing hydrologic and hydraulic (H&H) models.
Estuary
Temperature
Nutrients
Dissolved Oxygen
Algae
Metals
Contaminants
Key:
ERDC
HEC

## Slide 10: Model Dimensions: River-Floodplain System
Unstratified river channels are often modeled as one-dimensional (1D) water bodies, varying from upstream to downstream
Hydrologic connectivity across the floodplain is important
Floodplains need to be modeled as two-dimensional (2D) water bodies, varying in all directions across the landscape
1D River (Channel)
2D River (Floodplain, Wetlands)
Graphics by Lauren Melendez

## Slide 11: ClearWater-Riverine: 2D Water Quality Modeling with HEC-RAS and GSSHA
ClearWater Modules:
  Compute heat budget and constituent kinetics for a single cell
ClearWater Engine:
  Computes advection-diffusion across the model grid at each time step
ClearWater Framework:
  Links water quality and ecological models with water resources models
  Controls
    Model input and output
    Time steps (computational, input, and output)
    Simulation of transport across the model grid
  Coordinates engine, modules, and data
Inputs
  Volumetric flows, velocities, depths
  Model grid (bathymetry)
  Observed meteorology and water quality time series
Outputs
  Time series of 2D water quality grids, one time series per variable
  Time series of simulated hydrodynamic and water quality data at user-selected locations
2D Water Quality Model
Notes: EMRRP funded HEC-RAS water quality (1D) and ClearWater-Riverine (linked with HEC-RAS-2D).
The Next Generation Ecological Modeling project funded expanding ClearWater-Riverine to support linking with GSSHA and ecological models.

## Slide 12: Developing Python versions of TSM & NSM
Isaac and Kelsey

## Slide 13: Nutrient Simulation Module (NSM) Processes
Zhang & Johnson, 2016
Notes: Relevance to ecology: spatial patterns of dissolved oxygen, algal carbon production, nutrient control of plant growth.

## Slide 14: Developing new Python-based Modules
Legacy NSM and TSM written in Fortran
New versions of NSM and TSM written in Python
  Single cell calculations
  Python framework will iterate computations for multiple cells
Notes:     Adopted algorithms from legacy versions of NSM and TSM, porting from Fortran to Python
    Focus on calculating a single cell and single timestep
      Reaction calculations only need to know state variables (concentrations, temperature, etc.) in that cell at that time.
    Then convert to modern Python framework to extend calculations in multiple dimensions, handle I/O, and couple with other models
      Anthony will describe this in more detail below

## Slide 15: Temperature Simulation Module (TSM) Processes
Zhang & Johnson, 2016
Notes: Relevance to ecology: spatial patterns of dissolved oxygen, algal carbon production, nutrient control of plant growth.

## Slide 16: Testing TSM and Path Forward for NSM
We tested the implementation of TSM by recreating the kinetic equations in Excel as well as comparing to the Fortran water quality modules developed by ERDC and HEC for HEC-RAS (1D).

## Slide 17: Framework and Model Coupling
Anthony

## Slide 18: Modern Scientific Python
Built using the cloud-native geospatial Python stack being widely adopted by NOAA, USGS, NASA, etc.
An object-oriented architecture inspired by xarray-simlab / fastscape and CSDMS LandLab
Automated unit testing
https://numfocus.org/sponsored-projects
Notes: This [modern, cloud-native, geospatial Python] stack is designed to scale computations from a single set of values to multi-dimensional arrays, as shown in the icon for the xarray package, and scale from laptop to parallel computing to distributed cloud computing, powered by the Dask library that is built-in under-the-hood for xarray. All these libraries are very well supported by foundations, industry, and federal agencies.
We also wanted to follow modern numerical modeling coding patterns in widespread use by the geosciences community, so we we organized

## Slide 19: Model Coupling
Basic Model Interface (BMI)
  Provides a common set of functions
    To run models and exchange information and data on grids, variables, timesteps, etc.
  Shares data among models using a zero-copy approach
    Each model reads and writes to the same in-memory object using pointers
  Supports models written in C, C++, Fortran, Java, Python, Javascript, Julia
    NOTE: BMI must be implemented in the source code of a model before it can be used to couple that model to other BMI-compliant models
  Learn more: https://bmi.readthedocs.io
Modeling community moving toward systems of coupled models from modular model components.
BMI 2.0 has become the standard for model coupling

## Slide 20: Running Clearwater-Riverine and Clearwater-Modules Individually
Initialize Riverine
Create model mesh
Update Timestep
Advect and diffuse
Flow Field
Initial Conditions
Boundary Conditions
timestep = 0
timestep = 1…n
repeat n times
Initialize Modules
Create model mesh
Met Data
Topology, Volumes,
Surface Areas, Water Temp
Update Timestep
Energy Budget
repeat n times
Notes: Both Clearwater Riverine and Clearwater Modules can be run on their own (users can simulate transport only or reactions only).
Highlights that these are fully de-coupled.

## Slide 21: Running Clearwater-Riverine and Clearwater-Modules as Linked Models
Initialize Riverine
Create model mesh
Update Timestep
Advect and diffuse
Flow Field
Initial Conditions
Boundary Conditions
timestep = 0
timestep = 1…n
repeat n times
Initialize Modules
Inherit model mesh
Met Data
Topology, Volumes,
Surface Areas, Water Temp
Update Timestep
Energy Budget
Volumes,
Surface Areas, Water Temp
Water Temperature
Notes: Coupling the models:
- Modules inherits the mesh and some initial conditions from Riverine
- Information is passed between the models over time (timesteps 1…n)
- Both are being developed with BMI in mind for easy coupling
- Riverine could be updated to pair with any flow field
- Modules could be coupled with any model

## Slide 22: Clearwater Demonstration
Sarah

## Slide 23: Demo Case Study: Sumwere Creek — Domain & Mesh
Coarse Mesh Fine Mesh
Notes: Flow field is from HEC RAS-2D output in this case
Domain: 200 meters by 200 meters
Fictitious Topography/Bathymetry
  - Bathymetry bottom elevation constant at 20 m
  - Floodplain elevation constant at 24 m
  - Roadway elevation constant at 26 m
Two Unstructured Meshes Tested
  - Coarse Mesh: Base Mesh of 10 m by 10 m
  - Fine Mesh: Base Mesh of 4 m by 4 m with a 2 m by 2 m refinement within the creek

## Slide 24: Demo Case Study: Sumwere Creek — Hydrodynamic Boundary Conditions
Coarse Mesh Fine Mesh
Upstream: 3 cms
Spring:
1 cms
Powerplant:
0.5 cms
Downstream:
20.75 m
Notes: HEC-RAS Boundary Conditions
  - Upstream Flow for Sumwere Creek constant at 3 cms (1st hour ramping from zero)
  - Downstream Stage for Sumwere Creek constant at 20.75 m
  - Flow for Cold Spring Creek constant at 1 cms (1st hour ramping from zero)
  - Flow for Power Plant Chute constant at 0.5 cms (1st hour ramping from zero)

## Slide 25: Demo Case Study: Sumwere Creek – Depth at Start of Simulation
Coarse Mesh Fine Mesh
Notes:   HEC-RAS Initial Conditions
  - Initial Water Surface Elevation of 20.75 m set

## Slide 26: Demo Case Study: Sumwere Creek — Depth at End of Simulation
Coarse Mesh Fine Mesh
Notes: Depth results for both meshes in plan view do not show the differences very well…

## Slide 27: Demo Case Study: Sumwere Creek — Depth at End of Simulation
Notes: Profile of the coarse and fine mesh depth results along the magenta line in the plan view plot.
This shows the depth at the upstream boundary at 1.27 m and 1.23 for the coarse and fine mesh, respectively (4 cm difference); these depth difference are due to mesh resolution. This shows approximately 0.5 m of hydraulic head is required to overcome the bed friction for this flow rate. A uniform Manning’s roughness coefficient of 0.06 was used in both meshes.

## Slide 28: Demo Case Study: Sumwere Creek — Velocity at End of Simulation
Coarse Mesh Fine Mesh
Notes: Differences in velocities between the meshes are due to varying spatial resolution in each mesh

## Slide 29: Demo Case Study: Sumwere Creek — TSM Temperature Boundary Conditions
Coarse Mesh Fine Mesh
Upstream: 15˚C
Spring:
5˚C
Powerplant:
20-25 ˚C
Notes: Boundary conditions are the same for both the coarse and the fine mesh.
Designed to show longitudinal mixing across the river
Exploration of different extremes (cool water from spring-fed tributary versus warm water from powerplant)

## Slide 30: Demo Case Study: Sumwere Creek — TSM Temperature Boundary Timeseries
Coarse Mesh
Upstream: 15˚C
Spring:
5˚C
Powerplant:
20-25 ˚C
Notes: Timeseries of boundary conditions (stable, except for powerplant discharge)
Powerplant discharge has two peaks during the day (one in the morning, one in the afternoon)

## Slide 31: Demo Case Study: Sumwere Creek — TSM Meteorological Timeseries
Notes: Meteorological timeseries used as inputs to TSM.
Air temperature and solar heat flux both peak during the day and drop at night.
Timeseries from Arizona (extreme cycles to help capture impact of TSM).

## Slide 32: Results – Model Spin-Up
Coarse Mesh Fine Mesh
Notes: Some model spin-up to reach steady-state conditions.
Set initial conditions to 15C everywhere.

## Slide 33: Results – Model Spin-Up
Coarse Mesh Fine Mesh
Notes: You can see the mixing.
Ultimately reaches steady state.

## Slide 34: Results – Warm Powerplant Inflows
Coarse Mesh Fine Mesh
Notes: Pulses from powerplant.
Can see a lot more transverse mixing from the powerplant and spring in the fine mesh compared to the coarse mesh.
Can see more detail on the plume of warm water.
This all shows transport very clearly, but what about our energy budget model / TSM?

## Slide 35: Results – Impact of TSM
Coarse Mesh
TSM: cyclical rise and fall of water temperature (solar heat flux, air temp)
Upstream: 15˚C
Notes: Let’s take a look at a single cell. We have steady boundary conditions upstream, so without TSM, water temperature would also be steady over time
But we are coupling with TSM, so we see the cyclical rise and fall of water temperature due to our changes in solar heat flux and air temperature.

## Slide 36: Results – Impact of TSM
Coarse Mesh
TSM: impacts are still apparent in downstream mixing zones
Powerplant: 20-25˚C
Notes: The impacts of TSM are apparent even in mixing zones
Dominant visual is the peaks from powerplant discharges, but you can see the daily rise and fall still as an underlying trend.

## Slide 37: Results – Interactive Visualization
Python framework allows easy integration with powerful interactive visualization packages
  Enhanced understanding of complex environmental/ecological outcomes
  Iterative analysis and scenario discovery
  Multidimensional exploration across time and space
  Effective communication of results across teams and stakeholders
source
Notes: Building on the shoulders of giants.
We do not build or maintain any of these libraries.

## Slide 38: Results – Interactive Visualization Live Demo
Notes: Live demo; Sarah to screen share.

## Slide 39: Summary
ClearWater was expanded to simulate nutrient and temperature flow
Flexible framework designed to link:
  Water Quality models
  Vegetation models
  Water Resources models
    HEC-RAS (2D)
    GSSHA
Demonstration showed simulation of heat transport in a complex riverine system

## Slide 40: Benefits
Improved understanding of how nutrient dynamics influence species distribution patterns
Informs invasive species management
Enhanced ability to predict and develop targeted ecosystem restoration strategies based on nutrient availability and species responses
Better insights into the role of nutrient cycling in ecosystem functioning (e.g., primary productivity)
Supports informed management decisions
Improves prediction of carbon cycling (e.g., supports carbon sequestration analyses)

## Slide 41: Implications for Next Generation Ecological Modeling
Model linking using BMI enables a seamless exchange of data and information between different components of the integrated modeling system.
Facilitates data-driven decision-making
Enhances collaboration between scientific disciplines
Integrated models that simulate the interactions between heat, nutrients, water flow, and vegetation enable a comprehensive representation of ecosystem dynamics.
  Accurate representation of real-world processes
Enables assessment of the ecological responses to various environmental changes, such as land use modifications, climate change, or nature-based feature design and Best Management Practices (BMPs)
Example applications:
  Setting nutrient loading limits
  Designing buffer zones
  Implementing BMPs to restore aquatic ecosystems

## Slide 42: Questions?