## Slide 1: Development of a Predictive HAB Planning Tool using CE-QUAL-W2 Todd Steissberg (Todd.E.Steissberg@erdc.dren.mil, 530-574-5572) Jodi Ryder, Isaac Mudge, Emily Summers, Lauren Melendez
  ANSRP Harmful Algal Bloom Congressional Interest In-Progress Review
Problem: Existing models inadequately predict the timing, frequency, intensity, spatial variability, and impacts of Harmful Algal Blooms (HABs).
Solution: Develop a predictive HAB planning tool using ERDC’s reservoir water quality model, CE-QUAL-W2.

## Slide 2: CE-QUAL-W2
CE‐QUAL‐W2 is a two‐dimensional (2D), longitudinal/vertical, hydrodynamics and water quality model that enables characterization of vertical and longitudinal changes in reservoirs.
The model assumes reservoirs are well mixed laterally, with no variation from one channel side to the other in a layer (vertical) and segment (longitudinal).
CE-QUAL-W2 has been applied to rivers, lakes, reservoirs, and estuaries.
Ecological Modelling 466 (2022) 109888

## Slide 3: CE-QUAL-W2 Capabilities
Longitudinal-vertical hydrodynamics and water quality in stratified and non-stratified systems
Nutrients-dissolved oxygen-organic matter interactions
Fish habitat
Selective withdrawal from stratified reservoir outlets
Hypolimnetic aeration
Multiple algae, epiphyton/periphyton, zooplankton, and macrophytes
CBOD
Sediment diagenesis model
Generic water quality groups
Internal dynamic pipe/culvert model
Hydraulic structures (weirs, spillways) algorithms, including a dynamic shading algorithm based on topographic and vegetative cover.
Water age – Useful for forensic analyses

## Slide 4: Past and Current Applications of CE-QUAL-W2
CE-QUAL-W2 is widely used by USACE and other federal, state, and local agencies for environmental impact assessments, planning studies, etc. Agencies that use CE-QUAL-W2 as their standard reservoir water quality model include:
  U.S. Geological Survey (USGS)
  U.S. Bureau of Reclamation
  U.S. Environmental Protection Agency (EPA)
  State of California
More than 1,100 model applications have been developed worldwide for reservoirs, rivers, estuaries, and other water bodies since CE-QUAL-W2 was released in 1986.
CE-QUAL-W2 is also used as a research tool by researchers at universities and other organizations.
At least 1,500 publications utilized or cited CE-QUAL-W2 in the year 2022 alone.
Recent Studies:
  Water Temperature Modeling Platform, California Central Valley Project (USBR and State of California): This platform applies CE-QUAL-W2 for ongoing and future operations decision-making
  USACE Northwest Division, Columbia and Snake River Watershed
    Columbia System Reservoir Operation (CRSO) Project
    Columbia River Treaty (CRT) Project
  Philadelphia District, Lehigh River Water Quality Modeling
Region of Application:
Water Temperature Modeling Platform
California Central Valley Project

## Slide 5: CE-QUAL-W2 Benefits
Since it was first released in 1986, CE-QUAL-W2 has been used by water quality managers to assess impacts of management strategies on reservoir, lake, and estuarine systems.
CE-QUAL-W2 computes the two-dimensional velocity field for narrow systems that stratify.
In contrast with reservoir models with simplified hydrodynamics, CE-QUAL-W2 accurately simulates vertical and longitudinal transport of constituents, which can be as important as chemical kinetics in accurately simulating water quality.
Applications of CE-QUAL-W2 include:
  Planning Studies
  Environmental Impact Assessments
  Ecosystem Restoration Projects
  Real-Time Systems Operation and Decision-Making

## Slide 6: Challenges and Solutions
Developing HAB simulation capabilities applicable to any reservoir is challenging. Reservoirs have characteristics that can vary significantly:
  Algal species
  Water body morphometry (length, width, etc.)
  Volume
  Depth
  Mixing dynamics (wind forcing, fetch orientation)
  Harmful algal blooms can exhibit rapid changes and non-linear dynamics that are difficult to capture in model simulations.
To address these issues:
  Extensive literature and model review.
  Gather ideas from HAB experts.
  Case study site (Detroit Lake) selected to provide adequate data and a range of conditions that enables development of scaling methods.
  Consider focusing on one species and generalizing as far as possible to use it as a surrogate for prediction.
Detroit Lake, Oregon
Detroit Lake HAB

## Slide 7: Method and Algorithm Research
Upwelling and boundary mixing dynamics
  HABs are not spatially uniform
  They are controlled by light penetration, temperature, and nutrient availability
  Investigate the role of boundary mixing and upwelling on light penetration and HAB growth
  Relate vertical mixing to HAB occurrence and intensity
    Nondimensional numbers: Schmidt Stability Index, Wedderburn Number, Richardson Number

## Slide 8: Method and Algorithm Research
CE-QUAL-W2 enhancements:
  HAB species growth dynamics
  Vertical diurnal migration
  Nitrogen fixation algorithms (cyanobacteria may outcompete native algae since they can fix nitrogen)
  Sub-grid modeling to capture lateral variability (post-processing tool)
Prediction tool:
  Use CE-QUAL-W2 outputs and observed cross-sectional data to predict the maximum concentrations and locations of occurrence.

## Slide 9: Benefits
The CE-QUAL-W2 HAB prediction tool will simulate HAB occurrences with greater precision.
The tool will provide a real-time understanding of how various environmental factors contribute to HAB dynamics, allowing for timely assessments that can lead to more proactive management.
The data generated will be instrumental in formulating effective mitigation strategies, potentially reducing the frequency and severity of HAB events by targeting identified key contributing factors.
The outputs will facilitate adaptive management practices, where strategies and responses can be continuously refined based on the latest predictive insights.
Accurately simulating HAB events for multiple possible future conditions will improve emergency response protocols, aiding in the preparation and deployment of resources to affected locations efficiently.

## Slide 10: Benefits
Through early detection and management of HABs, the model will help protect ecosystem health and public safety, minimizing the adverse effects on wildlife and human populations.
By preventing or minimizing HAB occurrences, the model will indirectly aid in safeguarding local economies dependent on water-related industries such as fisheries, tourism, and recreation.
The outputs will improve communication and help to engage and educate stakeholders, including local communities, policymakers, and environmental organizations, fostering collaboration in HAB management efforts.
The development and refinement of the CE-QUAL HAB models represent significant scientific and technological progress in the field of ecological modeling and environmental management.