## Slide 1: Water Quality Modeling and Analysis Capabilities for River, Reservoir, and Watershed Management and Restoration
Jodi Ryder, PhD, Research Civil Engineer
Todd Steissberg, PhD, PE, Research Environmental Engineer
Environmental Laboratory
Engineer Research and Development Center (ERDC)
U.S. Army Corps of Engineers
Thai Royal Irrigation Visit
July 2025
UNCLASSIFIED
UNCLASSIFIED

## Slide 2: Water Quality Model Development
Todd to fill in this section with 2-5 slides
Plan
-Welcome - 1 min- Jodi in person
title slide
-Overview of integrated model development - 5 mins - Todd online
-Applications - 1 or 2 conscience example - here's how you take those tools and make them site specific - 5 mins - Jodi and Todd
-End with Conowingo sediment bucket to look at - integrating real system information into model - In person - Jodi - 3 mins
-Questions and transition to sediment lab 5 mins - All

## Slide 3: Water Quality and Environmental Systems Modeling
Water quality modeling tools:
  Watershed Runoff:
    GSSHA: Surface and sub-surface water quality modeling
    HEC-HMS: Surface runoff temperature modeling
    SWAT: Soil Water Assessment Tool
  Reservoirs:
    CE-QUAL-W2: 2D reservoir-river hydrodynamics and WQ modeling
    HEC-ResSim: Reservoir operations and water quality modeling
  Rivers and Floodplains:
    HEC-RAS: 1D River hydraulics and WQ modeling
    ClearWater-Riverine: 2D River-floodplain hydraulics and water quality modeling with HEC-RAS-2D
ERDC’s Corps Library for Environmental Analysis and Restoration of Watersheds (ClearWater) provides environmental simulation capabilities that leverage existing hydrologic and hydraulic (H&H) models.
Estuary
Temperature
Nutrients
Dissolved Oxygen
Algae
Metals
Contaminants
Key: ERDC-EL – ERDC-CHL – HEC – USDA

## Slide 4
Reservoir Water Quality Modeling

## Slide 5: CE-QUAL-W2
CE‐QUAL‐W2 is a two‐dimensional (2D), longitudinal/vertical, hydrodynamics and water quality model. It enables characterization of the vertical and longitudinal changes in a reservoir. The model assumes the reservoir is “well mixed” laterally, with no variation from one side of the channel to the other in a given layer (vertical) and segment (longitudinal).
CE-QUAL-W2 has been applied to rivers, lakes, reservoirs, estuaries, and combinations thereof.
CE-QUAL-W2 incorporates the following water quality capabilities:
  Longitudinal-vertical hydrodynamics and water quality in stratified and non-stratified systems
  Nutrients-dissolved oxygen-organic matter interactions
  Fish habitat
  Selective withdrawal from stratified reservoir outlets
  Hypolimnetic aeration
  Multiple algae, epiphyton/periphyton, zooplankton, and macrophytes
  CBOD
  Sediment diagenesis model
  Generic water quality groups
  Internal dynamic pipe/culvert model
  Hydraulic structures (weirs, spillways) algorithms, including a dynamic shading algorithm based on topographic and vegetative cover.

## Slide 6: Harmful Algal Bloom Simulation with CE-QUAL-W2
Harmful algal blooms (HABs) pose a growing threat to water quality, ecosystem health, and water resource operations.
Four new capabilities were implemented in CE-QUAL-W2 to improve its ability to simulate HABs.
  Minimum algae concentration enforcement
  Mechanical removal of algae (e.g., harvesting)
  High algal mortality under hypoxic conditions
  Nitrogen fixation by algae
Benefits:
  Improved HAB simulation accuracy under a wider range of conditions and treatments
  Improve understanding of how various environmental factors contribute to HAB dynamics, enabling more proactive management
  Improve mitigation strategies to reduce the frequency and severity of HAB events by targeting identified key contributing factors
  Facilitate adaptive management practices
Improve HAB simulation of multiple future scenarios will improve emergency response and sampling
Improve early detection and management of HABs,which will help protect ecosystem health and public safety, minimizing the adverse effects on wildlife and human populations

## Slide 7: HEC-ResSim Water Quality Model (1D)
Visualization
Specifying Boundary Conditions
Model Geometry
Constituent Relation Parameters
Operating Rule Priorities
Scripted Rules and State Variables

## Slide 8: Temperature and Dissolved Oxygen Simulation with HEC-ResSim Russian River, California Prepared by RMA for the Sonoma County Water Agency
Temperature
Dissolved Oxygen
Lake Sonoma
Lake Mendocino
Temperature
Dissolved Oxygen

## Slide 9: Riverine Water Quality Modeling

## Slide 10: ClearWater: Next Generation Integrated Water Quality Modeling
ClearWater: Corps Library for Environmental Analysis and Restoration of Watersheds
  Provides water quality capabilities that link with or extend existing water resources models.
ClearWater-Riverine is a new two-dimensional (2D) river water quality model.
  The ClearWater-Riverine water quality model simulates temperature and advanced nutrient cycling in branching river systems and floodplains, incorporating hydrodynamic, water quality, and meteorologic inputs from multiple data sources and models.
  It utilizes existing HEC-RAS 2D models to define the model grid and compute the hydraulic information (flows, depths, velocities).
Runoff
Reservoirs
Rivers

## Slide 11: Demo Case Study: Somewhere Creek — Velocity at End of Simulation
Coarse Mesh Fine Mesh
Notes: Differences in velocities between the meshes are due to varying spatial resolution in each mesh

## Slide 12: Results – Animation
Coarse Mesh Fine Mesh
Notes: You can see the mixing.
Ultimately reaches steady state.

## Slide 13: Results – Warm Powerplant Inflows
Coarse Mesh Fine Mesh
Notes: Pulses from powerplant.
Can see a lot more transverse mixing from the powerplant and spring in the fine mesh compared to the coarse mesh.
Can see more detail on the plume of warm water.
This all shows transport very clearly, but what about our energy budget model / TSM?

## Slide 14: Nutrient Modeling Capabilities
Dissolved Oxygen
Ammonia (NH4)
Nitrate (NO3)
Total Inorganic Phosphorus (TIP)
Notes: Pulses from powerplant.
Can see a lot more transverse mixing from the powerplant and spring in the fine mesh compared to the coarse mesh.
Can see more detail on the plume of warm water.
This all shows transport very clearly, but what about our energy budget model / TSM?

## Slide 15: ClearWater-Riverine: E. Coli Transport in the Ohio River

## Slide 16: Water Quality Model Application
“All models are wrong, some are useful”
–George Box, 1976
Specific constituents
Habitat conditions
  Temperature, Salinity, DO, TDG, Turbidity
  Nutrient water quality
  N, P, C, S
Contaminants
  Metals, organics, bio-toxins
Specific conditions
Historical events
Event impacts
  HABs, Wildfires, Hurricanes
  Invasive species introduction
  Weather dynamics and meteorological trends
  Beavers
Management decisions
  New infrastructure
  New operations

## Slide 17: Using CE-QUAL-W2 to simulate impacts of future conditions
Source: Oregon Watershed Enhancement Board. (2024). Region 3 Observed & Projected Climate Changes. Oregon.Gov Water and Climate Resources. Retrieved November 19, 2024, from https://www.oregon.gov/oweb/resources/Pages/Water%20and%20Climate.aspx
Scenario 1 (Base): Model setup for 2013
Projected for Willamette Basin, Oregon by 2100:
Annual increase in stream temperature of 2.2°C
Annual air temperature increase of 2 - 6 °C
Increase in Winter precipitation
Decrease in precipitation during growing season
Scenario 2: Riverine inflow T + 2.2 °C
Scenario 3: Air T + 4 °C
Scenario 5: Combine all changes
Scenario 4: Inflow quantity +10% December-March
& Inflow quantity -10% April-July
Notes: The US Army Corps of engineers currently has a model setup for Detroit reservoir, which has been calibrated and validated for 2013. I’m not going to get too deep into the setup of W2, but if you’re interested in how it is setup or how we represent algae, come see me after.
The following bullets show projections for the Willamette region of Oregon released by the Oregon Watershed Enhancement board. We used these kind of as a basis for our first few run scenarios.

## Slide 18: Future projections show stronger stratification earlier in the year
Extent of Stratification
More stratified
Less stratified
Notes: In order to look at changes in reservoir stability, we have developed a stratification index. This is something that is especially important to look at for harmful algal blooms, which can be heavily dependent on stratification. If you’re interested in how we calculated this, we have a paper out in the Journal of Environmental Management.
The most important change to note occurs from February to June. At the beginning of the year there, you can see that increase in stratification from the base to the combination run. This indicates likely earlier onset of stratification for Detroit reservoir in the decades to come.

## Slide 19: Overall changes to temperature structure
Cold surface pool disappears at beginning of year
Higher surface temperatures earlier in the year
Deeper penetration of warmer water further into the year
Current conditions
Projected conditions
Notes: We went ahead and generated some temperature profiles to see if overall heat structure in the lake changed. The left is conditions for the normal 2013 run and the right is the projected conditions with all the combined changes. While the patterns look similar, there are a couple important distinctions to note.
Its also important to note that max depth of the reservoir increased from 105 meters to 106 meters.

## Slide 20: Impact on Algal Blooms
Chlorophyll-a
Earlier onset
of blooms
“All models are wrong, some are useful”
–George Box, 1976
Notes: The combination of the three conditions resulted in a bloom two weeks earlier, but about the same magnitude as the original. One important thing to note is that there was an influx of nitrogen into the system at the end of may, which likely prompted the original bloom. If more nutrients were available earlier in the year, especially under future conditions, its likely we will be seeing worse blooms, more towards the beginning of may.

## Slide 21
Parameterizing Models
Modeling impacts of storm scour and selective dredging at Conowingo Reservoir, Maryland
Critical component is the influence of sediment on nutrient water quality in the water column
Customized lab analysis to populate model

## Slide 22: Team up on Water Quality and Contaminant Modeling Solutions
USACE-ERDC-EL-EPW
Water Quality and Contaminant Modeling
Jodi L. Ryder
Jodi.L.Ryder@usace.army.mil
601-631-1852
Todd E. Steissberg
Todd.E.Steissberg@usace.army.mil
530-574-5572
Brooke S. Weaver
Branch Chief EPW
Brooke.S.Weaver@usace.army.mil
601-634-3705
Programs and Partners