## Slide 1: Anticipating threats in natural Systems
Integrated Risk-Based Environmental Modeling of Extreme Coastal Weather Events
Dr. Todd Steissberg (ERDC-EL)
Dr. Matt Smith (USACE-IWR)
Ms. Marriah Abellera (USACE-IWR)
Dr. Jennifer Olszewski (ERDC-EL  USGS)
Mr. Isaac Mudge (USACE New Orleans District)
Anthony Aufdenkampe (LimnoTech)
Sarah Jordan (LimnoTech)
Jason Rutyna (LimnoTech)
OTHERS?
UNCLASSIFIED
ACTIONS IPR Meeting, September 24, 2024

## Slide 2: Objective: Integrated Hydro-Ecological Modeling
Develop integrated hydro-ecological models that simulate the complex and dynamics interactions between hydrology, meteorology, climate, water quality (salinity, temperature, nutrients), soil chemistry, vegetation, and morphology processes.
Models will enable evaluating system vulnerabilities and identifying adaptation pathways to improve the resilience of coastal ecosystems to environmental stresses, such as increasing frequency and intensity of coastal storm surges and extreme precipitation events, rising sea levels, decreasing freshwater flows, and increased salinity intrusion.

## Slide 3: Objective: Integrated Hydro-Ecological Modeling
Models will incorporate process descriptions from the other ACTIONS teams to provide the ability to simulate future conditions and provide more rigorous design tools for construction of Nature Based Features (NBF).
Provides tools for Engineering with Nature (EWN) projects that accurately simulate future conditions with and without projects at the temporal and spatial scales necessary for engineering design

## Slide 4: Environmental Modeling Tasks
Environmental Forcing Models
Simulate combinations of environmental forcing conditions to generate a plausible range of coastal hazards while preserving the complex interaction between contributing processes
Water Quality Models
Ecological Models
Relate indicator species responses - e.g., growth and health to water balance components, soil conditions, surface and subsurface water quality - to environmental forcing
Simulate watershed and riverine water quality and contaminant release from soils under saline conditions

## Slide 5: FY25 Accomplishments
Water Quality Model
Completing development of the ClearWater-Riverine Model
  Leverages HEC-RAS 2D models
    Model grid
    Hydrodynamics of simple and complex river systems
      River channel
      Flood plains
      Braided rivers
      Riparian buffers
  Simulates water temperature and quality (nutrients, algae, dissolved oxygen) and their flow through ecosystems

## Slide 6: FY25 Accomplishments
Water Quality Model
TBD: memory and speed improvements, gate feature, etc.

## Slide 7: FY24 Milestones and Products
Salt Marsh Model
  Q4/FY25 (Deliverable): Hydroecological Salt Marsh Model
  Q4/FY25 (Deliverable): Dotson Family Marsh case study model for baseline conditions. This case study couples Delft 3D hydrodynamics + waves, NBSDynamics vegetation, and the NETHERLAND morphology models.
  Q4/FY25: Technical Note on the salt marsh model and case study

## Slide 8: Water Quality and Environmental Systems Modeling
Water quality modeling tools:
  Watershed Runoff:
    GSSHA: Surface and sub-surface water quality modeling
    HEC-HMS: Surface runoff temperature modeling
  Reservoirs:
    CE-QUAL-W2: 2D reservoir-river hydrodynamics and water quality modeling
    HEC-ResSim: Reservoir operations and water quality modeling
  Rivers and Floodplains:
    HEC-RAS: 1D River hydraulics and water quality & vegetation modeling
    ClearWater-Riverine: 2D River-floodplain hydraulics and water quality modeling with HEC-RAS-2D
ERDC’s Corps Library for Environmental Analysis and Restoration of Watersheds (ClearWater) provides environmental simulation capabilities that leverage existing hydrologic and hydraulic (H&H) models.
Estuary
Temperature
Nutrients
Dissolved Oxygen
Algae
Metals
Contaminants
Key: ERDC-EL – ERDC-CHL – HEC

## Slide 9: ClearWater: Next Generation Integrated Water Quality Modeling
ClearWater: Corps Library for Environmental Analysis and Restoration of Watersheds
Purpose: Link environmental models with existing water resources models that simulate runoff, rivers, and reservoir hydraulics and hydrology
ClearWater provides environmental simulation capabilities that are designed to leverage existing water resources models.
  The ClearWater water quality modules simulate constituent kinetics, heat budget processes, and vegetation growth cycles. Capabilities include:
    NSM: Nitrogen, phosphorus, and carbon cycling; dissolved oxygen, algae, etc.
    TSM: Temperature (heat budget)
    GSM: General Constituents
    CSM: Organic and inorganic contaminants
    MSM: Mercury
ClearWater contains legacy modules written in Fortran and C++ and next-generation modules written in Python (NSM and TSM)
  Engine computes the transport (advection and diffusion) of heat and constituent mass across the watershed
  Data visualization capabilities
  Framework to integrate multiple models.
Runoff
Reservoirs
Rivers

## Slide 10: ClearWater-Riverine
ERDC’s new Clearwater-Riverine model simulates temperature and advanced nutrient cycling in branching river systems and floodplains, incorporating hydrodynamic, water quality, and meteorologic inputs from multiple data sources and models.
Water quality kinetics and heat budget are computed for each cell in a computational domain by ERDC's ClearWater modules.
The ClearWater-Riverine framework links the capabilities provided by the ClearWater modules and advection-diffusion engine with the two-dimensional (2D) HEC-RAS model.
ClearWater-Riverine will enable the evaluation of system vulnerabilities and identification of adaptation pathways to improve the resilience of riverine ecosystems to environmental stresses, which include increasing frequency and intensity of extreme precipitation events and decreasing freshwater flows.
HEC-RAS models have been developed for most of the watersheds around the world. By leveraging these existing models, ClearWater-Riverine provides a cost-effective, data-driven tool for impact assessment, planning studies, and the restoration and management of aquatic ecosystems.
Notes: The ERDC Environmental Laboratory (ERDC-EL) is at the forefront of developing a cutting-edge water quality modeling system called ClearWater-Riverine. This advanced system focuses on simulating temperature dynamics and advanced nutrient cycling in branching river systems and floodplains. It integrates inputs from multiple data sources and models, incorporating hydrodynamic, water quality, and meteorologic information.
The primary goal of ClearWater-Riverine is to assess system vulnerabilities and identify adaptation pathways that enhance the resilience of floodplain ecosystems to environmental stresses. These stresses include the increasing frequency and intensity of extreme precipitation events and decreasing freshwater flows. By accurately simulating water quality kinetics, heat budget, and transport, ClearWater-Riverine enables a comprehensive evaluation of the impacts on water quality and provides insights into potential mitigation and restoration strategies.
The modeling capabilities of ClearWater-Riverine are enhanced through the integration of ERDC's ClearWater modules. These modules provide the necessary functionalities for simulating water quality kinetics, heat budget, and transport processes. They form the foundation for the water quality simulations within the ClearWater-Riverine framework.
Furthermore, ClearWater-Riverine is designed to leverage the widely used two-dimensional (2D) HEC-RAS model. By linking the capabilities of ClearWater modules and the advection-diffusion engine with the 2D HEC-RAS model, ClearWater-Riverine combines the strengths of both systems. This integration allows for a cost-effective and data-driven approach to impact assessment, planning studies, and the restoration and management of aquatic ecosystems.
The availability of HEC-RAS models for numerous watersheds worldwide enhances the applicability and efficiency of ClearWater-Riverine. By utilizing existing HEC-RAS models, ClearWater-Riverine eliminates the need to develop new models from scratch. This approach streamlines the modeling process, reduces costs, and facilitates wider adoption of the system for various water resource management and restoration initiatives.
In summary, the development of ClearWater-Riverine by the ERDC-EL represents a significant advancement in water quality modeling. By simulating temperature dynamics and advanced nutrient cycling, integrating multiple data sources and models, and linking with the 2D HEC-RAS model, ClearWater-Riverine provides a powerful tool for impact assessment, planning, and ecosystem management in river systems and floodplains.

## Slide 11: ClearWater-Riverine
Clearwater-Riverine simulates temperature and advanced nutrient cycling in branching river systems and floodplains, incorporating hydrodynamic, water quality, and meteorologic inputs from multiple data sources and models.
  Flows: The model grid, volumetric flow, velocities, depths, diffusivity, etc. are provided by existing 2D water resources models.
  Modules: Water quality kinetics and heat budget simulation capabilities in ClearWater-Riverine are furnished by ERDC's ClearWater modules (e.g., NSM).
  Transport: The ClearWater transport engine computes advection-diffusion of heat and mass through the model network.
  Framework: The ClearWater framework links all the components together and performs the water quality compute sequence.
Currently design is based on decoupled modeling, i.e., the flows are pre-computed by the hydro models.

## Slide 12: Demo Case Study: Sumwere Creek — Domain & Mesh
Coarse Mesh Fine Mesh
Notes: Flow field is from HEC RAS-2D output in this case
Domain: 200 meters by 200 meters
Fictitious Topography/Bathymetry
  - Bathymetry bottom elevation constant at 20 m
  - Floodplain elevation constant at 24 m
  - Roadway elevation constant at 26 m
Two Unstructured Meshes Tested
  - Coarse Mesh: Base Mesh of 10 m by 10 m
  - Fine Mesh: Base Mesh of 4 m by 4 m with a 2 m by 2 m refinement within the creek

## Slide 13: Demo Case Study: Sumwere Creek — Hydrodynamic Boundary Conditions
Coarse Mesh Fine Mesh
Upstream: 3 cms
Spring:
1 cms
Powerplant:
0.5 cms
Downstream:
20.75 m
Notes: HEC-RAS Boundary Conditions
  - Upstream Flow for Sumwere Creek constant at 3 cms (1st hour ramping from zero)
  - Downstream Stage for Sumwere Creek constant at 20.75 m
  - Flow for Cold Spring Creek constant at 1 cms (1st hour ramping from zero)
  - Flow for Power Plant Chute constant at 0.5 cms (1st hour ramping from zero)

## Slide 14: Demo Case Study: Sumwere Creek — Temperature Boundary Conditions
Coarse Mesh Fine Mesh
Upstream: 15˚C
Spring:
5˚C
Powerplant:
20-25 ˚C
Notes: Boundary conditions are the same for both the coarse and the fine mesh.
Designed to show longitudinal mixing across the river
Exploration of different extremes (cool water from spring-fed tributary versus warm water from powerplant)

## Slide 15: Demo Case Study: Sumwere Creek — Temperature Boundary Timeseries
Coarse Mesh
Upstream: 15˚C
Spring:
5˚C
Powerplant:
20-25 ˚C
Notes: Timeseries of boundary conditions (stable, except for powerplant discharge)
Powerplant discharge has two peaks during the day (one in the morning, one in the afternoon)

## Slide 16: Demo Case Study: Sumwere Creek — Velocity at End of Simulation
Coarse Mesh Fine Mesh
Notes: Differences in velocities between the meshes are due to varying spatial resolution in each mesh

## Slide 17: Demo Case Study: Sumwere Creek — Meteorological Timeseries
Notes: Meteorological timeseries used as inputs to TSM.
Air temperature and solar heat flux both peak during the day and drop at night.
Timeseries from Arizona (extreme cycles to help capture impact of TSM).

## Slide 18: Results – Animation
Coarse Mesh Fine Mesh
Notes: You can see the mixing.
Ultimately reaches steady state.

## Slide 19: Results – Warm Powerplant Inflows
Coarse Mesh Fine Mesh
Notes: Pulses from powerplant.
Can see a lot more transverse mixing from the powerplant and spring in the fine mesh compared to the coarse mesh.
Can see more detail on the plume of warm water.
This all shows transport very clearly, but what about our energy budget model / TSM?

## Slide 20: Nutrient Modeling Capabilities
Dissolved Oxygen
Ammonia (NH4)
Nitrate (NO3)
Total Inorganic Phosphorus (TIP)
Notes: Pulses from powerplant.
Can see a lot more transverse mixing from the powerplant and spring in the fine mesh compared to the coarse mesh.
Can see more detail on the plume of warm water.
This all shows transport very clearly, but what about our energy budget model / TSM?

## Slide 21: ClearWater-Riverine Example: E. Coli Transport in the Ohio River

## Slide 22: Hydro-Ecological Salt Marsh Model
Long-Term Goal: Inform design guidelines for constructed salt marshes NNBF for specific performance levels of wave attenuation, erosion reduction, and habitat creation.
Objective: Develop a “unit” salt marsh model that can demonstrate how to:
Design salt marshes for specific performance objective(s) that are robust to range of potential future sea level and sediment input conditions
Quantify performance using measurable performance metric(s)
Identify those marsh parameters (e.g., platform depth, vegetation species dominance, etc.) to which performance is most sensitive to.
Lead to the development of generalized salt marsh model design guidelines

## Slide 23: FY24 Salt Marsh Model: Design
Flow diagram of our complete salt marsh model
Performance metrics we are computing

## Slide 24: FY24-25 Salt Marsh Model Case Study
Case Study Site: Dotson Family Marsh, San Pablo Bay
The Dotson Family Marsh is a 238-acre (96 ha) regional park on San Pablo Bay in the East San Francisco Bay Area city of Richmond, California.
In 2009 the East Bay Regional Parks District acquired the marsh site, adding it to Point Pinole Regional Shoreline.
A habitat restoration plan for 60 acres of wetlands and 90 acres of California coastal prairie was subsequently approved.

## Slide 25: FY24-25 Salt Marsh Model Case Study
Vegetation coverage, Dotson Family Marsh
The colors represent different species.
The site started out with no vegetation. This snapshot is a few years after installation.
Elevations, Dotson Family Marsh

## Slide 26: FY24-25 Salt Marsh Model Case Study
Map showing the larger model (Nederhoff et al. 2021) that we nested our salt marsh model into.
This larger model will be used to generate water level and wave boundary conditions for our smaller salt marsh model.

## Slide 27: FY25 Hydro-Ecological Model Development
Collaborating with Deltares and Drs. Matt Smith and Marriah Abellera (IWR) to explore the modeling of salt marshes with the goal of informing design for specific performance objectives.
Completed prototype of the dynamic salt marsh model. It dynamically couples
  Hydrodynamics (Delft3D)
  Waves (Waves-D)
  Vegetation (NBSDynamics)
  Morphology (SEMIDEC)

## Slide 28: FY25 Milestones and Products
TBD

## Slide 29: FY25 Publications
TBD

## Slide 30: Questions?