## Slide 1: Water Quality Modeling Capabilities Todd Steissberg and Billy Johnson Water Quality and Contaminant Modeling Branch Environmental Laboratory U.S. Army Engineer Research and Development Center (ERDC) June 2, 2020

## Slide 2: Integrated Environmental Modeling Tools
Hydraulics and Hydrology
Water Quality
Vegetation
Elevation, M
River Section
Reservoir
Estuary
Distance, M
Design with Natural Features

## Slide 3: Integrated Watershed Water Quality Modeling
f
HEC-HMS
Runoff
HEC-ResSim
Reservoir release decisions
HEC-RAS
River hydraulics
Linked together with
CWMS (real-time)
HEC-WAT (studies)
CE-QUAL-W2
2D Reservoir WQ
Clearwater modules and engine

## Slide 4: Water Quality and Ecological Modeling Capabilities
Clearwater (Computational Library for Environmental Analysis and Restoration of Watersheds) is a computational library that is being embedded in existing water resources simulation models.
  1. Modules that simulate water temperature, chemical reactions and transformations, and riparian vegetation. These modules are:
    NSM: Nutrient Simulation Module
    TSM: Temperature Simulation Module
    MSM: Mercury Simulation Module
    CSM: Contaminant Simulation Module
    SSM: Solids Simulation Module
    RVSM: Riparian Vegetation Simulation Module
      VSM: Vegetation Simulation Module (1D/2D riparian and aquatic vegetation)
  2. A water quality engine that computes the transport processes and integrates the Clearwater modules with the water resources simulation program (e.g., HEC-ResSim)
  3. Graphical User Interface (GUI) components for WQ modeling:
    Controls and tables to input/import set up a WQ model
      Boundary & initial conditions, variables, parameters, etc.
    Plots
    Reports

## Slide 5: Vision: Environmental Modeling with HEC Tools
The U.S. Army Corps of Engineers’ Water Quality Modeling Team is developing next-generation water quality modeling and analysis capabilities by integrating independent water quality modules with existing water resource modeling software. The team consists of staff from ERDC, HEC, USACE Districts, and other organizations. An ERDC-HEC partnership was established to develop water quality modeling capabilities for three widely used water resources modeling programs developed by the Hydrologic Engineering Center. These are:
  HEC-ResSim (Reservoir System Simulation): simulates reservoir operations for one or more reservoirs for flood management, planning studies, real-time decision support, and many other purposes.
  HEC-RAS (River Analysis System): simulates river hydraulics, computing water levels and velocities, and generates inundation (flood) maps
  HEC-HMS (Hydrologic Modeling System): simulates runoff from the watershed
HEC models have been built for most of the watersheds in the U.S. and for many of the watersheds in other countries. The water quality capabilities being developed for the HEC software leverages these models and existing software capabilities distribute advanced water quality modeling capabilities around the world. These will be linked, leveraging the strengths of each model to perform integrated watershed-scale water quality modeling for ecosystem assessment, restoration, and management.

## Slide 6
HEC-RAS River Water Quality (1D)
HEC-RAS (River Analysis System) simulates 1D and 2D river hydraulics
  Computes river velocities, stages, profiles, and inundated areas (with RAS Mapper) given stream flow and geometry
Industry standard hydraulic tool used worldwide
100,000 worldwide downloads/year
One-dimensional (1D) water quality capabilities allow environmental impacts assessments in rivers and streams

## Slide 7: Riparian Vegetation Simulation Module (RVSM)
The Riparian Vegetation Simulation Module (RVSM) simulates the lifecycle of vegetation, including seed dispersal, seedling establishment, and plant growth and mortality in response to dynamic physical conditions.
  RVSM includes eleven vegetation roughness computation methods.
Hydrologic Processes:

## Slide 8: HEC-RAS Riparian Vegetation Simulation
RVSM was integrated into HEC-RAS to simulate the interactions between flow and riparian vegetation on floodplains.
RVSM can help answer the following questions:
  What impact does riparian vegetation have on local flood conditions?
  What set of riverine operations can be used to encourage recruitment and survival of native vegetation (and control the spread of invasive species)?
  What impact will management actions have on habitat for endangered and threatened species?
For each time step:
  HEC-RAS computes water surface elevation, discharge, average velocity, energy slope of each cross section.
  RVSM simulates the impacts of these variables on the riparian vegetation lifecycle and computes the impacts of riparian vegetation on channel roughness (Manning’s n values).
  The new roughness values replace the previous values in the HEC-RAS model and are used to compute new hydraulic variables for the next time step.

## Slide 9: HEC-RAS Riparian Vegetation Simulation
Application:
  The riparian zone needs to be discretized into a vegetation computation mesh, including an array of parallel slice polygons along the channel bank.
HEC-RAS schematic with vegetation polygons:

## Slide 10
HEC-RAS - 2D Water Quality Two-Dimensional (2D) Depth-Averaged Water Quality

## Slide 11: HEC-ResSim Water Quality
Problem: Currently, water quality modeling is performed separately from reservoir operation decision-making, with results being laboriously transferred between models, which have to be repeatedly adjusted and recomputed to achieve environmental project objectives. Environmental considerations are not directly accounted for in reservoir operations decision-making, since existing reservoir water quality models cannot continuously inform reservoir operations models about how much water should be released meet these requirements.
Purpose: Integrate water quality modeling capabilities into HEC-ResSim so that water quality and related environmental objectives can directly influence reservoir release decision-making as well as providing capabilities for watershed-scale ecosystem assessment and management.
Flows influence water quality
Water quality must influence flows
Notes: We currently lack reservoir operations simulation software with the capability to fully integrate environmental objectives into reservoir release decision-making
  Water quantity and quality simulations are performed independently and sequentially in a one-way process
    Water quantity influences the water quality models
    However, water quality does not directly influence the computed releases. Influence and iteration is at the discretion of the modeler
This severely inhibits the ability to identify the most effective water management alternatives for meeting multiple objectives
WQ information is needed at every time step
EMRRP (Ecosystem Management and Restoration Research Program)
Approved by ERARG (Environmental Research Area Review Group

## Slide 12: HEC-ResSim Water Quality
New Approach
  WQ runs in parallel with the system hydrology and release decisions
  Reservoir operation rules can be specified directly (i.e., temperature, concentration, or load) to meet environmental objectives
  Project teams will have the opportunity to define rules for environmental objectives independent of other objectives,
Existing Approach
  WQ is simulated with an external model (e.g., HEC-5Q) after the HEC-ResSim flow simulation is complete.
  Rules are specified in terms of stage or flow.
  Environmental objectives are often lumped with other objectives, like navigation, flood control, or hydropower.
  If the desired environmental benefits of an alternative are not achieved, new guesses need to be made, and the simulation recomputed. This stage is often skipped altogether.
(Manually)

## Slide 13: HEC-ResSim v4.0

## Slide 14
Riverine zone
  River-like flows within channel
  Minimum requirement: 1D river model (segments)
Lacustrine zone
  Lake-like system, vertically stratified, slow flows
  Minimum requirement: 1D reservoir model (layers)
Transition zone
  Stratification and downstream flows important
  Minimum requirement: 2D model (layers and segments)
Reservoir system with important flow, WQ, and ecosystem processes for each of three zones.
Notes:
1D river model for channels in a reservoir system
2D river model for floodplain simulation
Reservoir Processes and Zones

## Slide 15
River-Reservoir System (stratification important)
  Unstratified reaches:
    Modeled as 1D rivers (segments)
  Stratified reaches:
    Can be modeled as 1D reservoirs (layers) for real-time release decision-making for downstream targets
    Need to be modeled as 2D reservoirs (layers and segments)
      Ensure accuracy, capturing important in-reservoir processes (mixing, pollutants inflows, etc.)
      Identify vulnerabilities and restoration/management options (e.g., velocities and temperature for HAB management)
River-Floodplain System (unstratified)
  River channels are modeled as 1D, varying from upstream to downstream
  Hydrologic connectivity across the floodplain is important
    2D varying across the landscape
Reservoir and River WQ Model Dimensions

## Slide 16
Capabilities
  HEC-ResSim incorporates 1D WQ in the reservoir release decision-making process
    Easy to use, modern graphics and user interface
  CE-QUAL-W2 simulates 2D reservoir WQ
    Accurately captures in-reservoir processes
    Widely used, many experienced users, many existing models
HEC-ResSim gaps:
  Lacks the accuracy of higher fidelity 2D WQ reservoir models
  Very limited applicability for reservoir studies
CE-QUAL-W2 gaps:
  Lacks operations capabilities, user interface, visualization & analysis capabilities
  Unstable for riverine reaches, limiting modeling watershed-scale reservoir systems
  Lacks an official ERDC version with proper QA/QC. Cannot currently be used for planning.
  Architecture and logic need to be updated to meet modern standards and computer capabilities (robust storage formats, parallel processing, etc.)
  Updated WQ algorithms need to be incorporated
  Very difficult to link with other models and ecosystem tools (needs improved data structures & input/output)
  Difficult to set up and operate (lacks user interface, input files easy to break)
CE-QUAL-W2 WQ profiles plotted using Python and matplotlib
Reservoir WQ Capabilities and Modeling Gaps

## Slide 17
Build 2D reservoir WQ modeling program capable of integrating environmental objectives into the reservoir decision-making process.
  Framework: Python and Jupyter notebooks
  Simulations: Fortran-based WQ engine
  Implement essential operations capabilities
Leverage CE-QUAL-W2 Program
  Leverage and upgrade CE-QUAL-W2’s hydrodynamics and WQ algorithms
  Restructure and upgrade code, data structures, and storage formats
    Improves robustness and facilitates linking with other models, ecosystem tools, etc.
Leverage ResSim WQ Program and Components
  Implement modern data structures and input/output files (HDF5, DSS, GeoJSON)
  Leverage code to read inflows, outflows, and WQ outputs from HEC-ResSim models
Leverage RAS 2D WQ Products
  Python framework and Jupyter notebook interface with inline documentation
  Storage formats for 2D data (HDF5) and parameters (JSON)
  Leverage plotting capabilities/components (time series, 2D animations, etc.)
  Note: Co-development of RAS 2D WQ and Reservoir 2D WQ is feasible and efficient. Components will be built that flexibly address river and reservoir modeling, visualization, and analysis needs.
Reservoir temperature model, showing variability along the river/reservoir channel
RAS 2D depths and velocities. Example product for RAS 2D WQ
CE-QUAL-W2 V5.0 Development

## Slide 18
Watershed Runoff Water Quality Modeling

## Slide 19: HEC-HMS Water Quality Objective
Build water quality modeling and analysis capabilities for HEC-HMS, in collaboration with ERDC Environmental Laboratory (ERDC-EL).
  Implement simulation of the water temperature and user-defined general constituents for:
    Overland flow
    Streams
    Reservoirs
This will form the foundation for a generalized next-generation watershed water quality modeling system capable of simulating non-point source water quality (nutrients, dissolved oxygen, phytoplankton, and bacteria) and characterizing its effects on the watershed.

## Slide 20: Watershed Runoff Water Quality GSSHA and SWAT
Extend nutrient simulation modules (NSMs) to extend salinity capabilities
Extend contaminant simulation module (CSM) for overland flow
Link NSMs and CSM with GSSHA
Link SWAT with river and reservoir models
Build plug-ins for HEC-WAT and CWMS

## Slide 21: Watershed-Scale Water Quality Modeling CWMS and HEC-WAT

## Slide 22: Corps Water Management System (CWMS)
Operational Decisions
Inundation Mapping
Real-Time Fully Integrated
Hydrologic Models
Streamgage
Data
NWS
Forecasts
Water quality development in HEC-ResSim, HEC-RAS, and HEC-HMS will provide real-time water quality capabilities in CWMS
CWMS (Corps Water Management System) provides real-time decision support for water management
700+ Multi-purpose reservoirs, flow control structures, levees, etc.
Features:
  Real-time data acquisition
  Database storage
  Flow forecasting of watershed runoff
  Reservoir operation decision support
  River profile modeling
  Inundated area determination
  Consequence/damage analysis
  Information dissemination
Implementation Goal: 201 CWMS systems by 2022

## Slide 23: HEC-WAT (Watershed Analysis Tool)
Hydraulics
Environmental
Hydrology
Reservoir
Consequences

## Slide 24
CE-QUAL-W2 Plug-In for HEC-WAT

## Slide 25
Hydrodynamics
Nutrient Cycles
Organism Growth
Transport Solvers
Output = Temporal and/or spatial distribution of modeled constituents
HEC-RAS (1D/2D WQ)
Observed Data
Model Outputs
Simulates reservoir operations at one or more reservoirs to meet multiple objectives for flood control, hydropower, water supply, navigation, recreation, and environmental management.
For both planning studies and for real-time decision support.
HEC-ResSim v4.0 has fully integrated water quality (WQ) modeling capabilities for environmental impacts analysis and operational support.
HEC-ResSim (1D WQ)
Fully integrated riverine hydraulic, sediment, and water quality model to aid users in determining Total Maximum Daily Loads (TMDLs).
Can be linked to SWAT and HSPF
USACE WQ Modeling: Watershed Systems Approach

## Slide 26
Example of interdependent nutrient cycles and algae growth
CE-QUAL-W2
AdH-NSM-2D/3D
2D, laterally-averaged hydrodynamic and water quality model, 28 constituents
Simulates stratified flow through variable density as affected by temperature, salinity, TDS, and TSS
Can be extended to model entire basins
Over 1600 known applications in 34 countries
CE-QUAL-ICM
Seamlessly integrates the Nutrient Simulation Module (NSM) library.
Several models available with varying degrees of coupling between the hydrodynamic, nutrient, organism, and transport algorithms.
Application domains range from run of river reservoirs to coastal zones.
First model to fully couple hydrodynamics and water quality on an adaptive mesh
  Includes floating and benthic algae, interrelated N, P, C, and O2 cycles
Surface Chlorophyll Concentration, mg/l
Fully 3D, time-variable; link to independent hydrodynamics
36 constituents
Elevation, M
River Section
Reservoir
Estuary
Distance, M
Trophic interactions include submerged aquatic vegetation multiple algae groups, sediment diagenesis, benthos, and zooplankton
USACE Water Quality Modeling Tools

## Slide 27: Team Members and Collaborators (Alphabetical)
Lea Adams, USACE-HEC
Mark Ackerman, RMA
Steven Ackerman, RMA
Steve Andrews, RMA
Chris Berger, PSU
Gary Brunner, USACE-HEC
Barry Bunch, USACE-ERDC-EL
Ben Chacon, RMA
Al Cofrancesco, ERDC-EL
John DeGeorge, RMA
Pat Deliman, ERDC-EL
Mark Dortch, ERDC-EL
Chris Dunn, USACE-HEC
Paul Ely, RMA
Scott English, USACE-NWD
Trudy Estes, ERDC-EL
Matt Fleming, USACE-HEC
Alex Kennedy, USACE-HEC
Joan Klipsch, USACE-HEC
John Kucharski, USACE-HEC  ERDC
Mark Jensen, USACE-HEC
Billy Johnson, USACE-ERDC-EL
Steve Juul, USACE-NWW
Shannon Larson, RMA
Cindy Lowney, RMA
Ryan Miles, RMA
Alexis Mills, USACE-NWD
Chan Modini, USACE-HEC
Shannon Newbold, RMA
Leila Ostadrahimi, USACE-HEC
Jay Pak, USACE-HEC
Steve Piper, RMA
Kervi Ramos, HEC/Apple  ERDC
Jodi Ryder, USACE-ERDC-EL
Alex Sanchez, USACE-HEC
Bill Scharffenberg, USACE-HEC
Don Smith, RMA
Todd Steissberg, USACE-ERDC-EL
Julia Slaughter, USACE-HEC
Kathryn Tackley, USACE-NWP
Tammy Threadgill, USACE-ERDC-EL
Dottie Tillman, USACE-ERDC-EL
Dan Turner, USACE-NWD
Scott Wells, PSU
Brian Zettle, USACE-SAM
Zhonglong Zhang, PSU/LimnoTech

## Slide 28: Thank You Questions?