## Slide 1
PDT Lead: Todd Steissberg (ERDC)
Product Development Team:
  Zhonglong Zhang (PSU)
  Scott Wells (PSU)
  John Kucharski (ERDC)
  Billy Johnson (ERDC)
  Barry Bunch (ERDC)
  Jodi Ryder (ERDC)
Corps District Collaboration:
  Brian Zettle (Mobile District, CoP Lead)
  Kathryn Tackley (Portland District)
  Dan Turner (Northwest Division)
  Alexis Mills (Northwest Division)
  Laurel Hamilton (Omaha District)
  Jim Noren (St. Paul District)
Development of New Capabilities and Enhancements to the USACE Two-Dimensional Reservoir Water Quality Model (CE-QUAL-W2)

## Slide 2: Project Purpose - Recap
This work unit was developed in response to SON ENV 1174, Development of New Capabilities and Enhancements to the USACE Two-Dimensional Reservoir Water Quality Model (CE-QUAL-W2), presented to the 2018 ERARG to address SON ENV 1550, Two-Dimensional Water Quality Capabilities for Reservoir Operations Decision-Making, presented to the 2020 ERARG.
Objectives:
Upgrade CE-QUAL-W2 to incorporate the latest water quality modeling R&D at ERDC
Restructure current CE-QUAL-W2 model source code to use robust data storage file formats that adhere to widely-supported modern standards, such as HDF5 and CSV, enabling seamless linkage with other models, e.g., HEC-RAS and HEC-ResSim, improving multi-model system reliability and reducing maintenance cost of software, models, and linked modeling systems.
Notes: Keep it simple and clear. You may use a second slide if needed, however.

## Slide 3: Project Purpose - Recap
Objectives, continued:
Decouple the WQ component from hydrodynamics in the current version of CE-QUAL-W2, allowing water quality simulations to run multiple times with the same hydrodynamic results, eliminating costly repeated hydrodynamic computations
Update the technical reference manual and user manual
Release comprehensive version of CE-QUAL-W2, reviewed by ERDC experts
Notes: Keep it simple and clear. You may use a second slide if needed, however.

## Slide 4: Benefits
The updated CE-QUAL-W2 model will support the Corps’ high priority need for environmental assessment, restoration, and management.
Incorporation of reservoir operations capabilities will enable water quality and other environmental objectives to influence reservoir release decisions, improving model accuracy and delivering high quality multi-objective decision-making to achieve ecosystem benefits.
  Critical downstream habitat will be better managed for water quantity (volume, velocity, depths, etc.) in addition to water quality (water temperature, dissolved oxygen, total dissolved gas, etc.).
  Linkage of WQ with multi-objective decision analysis increases project benefits while decreasing modeling and project costs.
Development of improved and accessible reservoir water quality modeling capabilities will reduce time and cost associated with upgrading water quality models and adding new model capabilities.
The new file formats improve model robustness and facilitate linking W2 models with other models.
Notes: Keep it simple and clear. You may use a second slide if needed, however.

## Slide 5: Approach
Incorporate new capabilities developed at ERDC-EL into the current CE-QUAL-W2 model maintained by PSU
  Develop and integrate a full carbon cycle with nitrogen and phosphorous cycles and integrate into the updated version
  Reformulate simulations of BOD groups (CBOD, NBOD, and PBOD) included in current version of W2 to ensure appropriate simulation of these constituents
  Upgrade the sediment diagenesis module and merge into the updated version for further testing and validation
  Add additional water quality state variables (CH4, H2S, SO4, Fe and Mn Species) into updated version
Task 1: Upgrade Water Quality Kinetics
Notes: Keep it simple and clear. Particularly with modeling efforts - the interaction of different models, modules and updates needs to be clear. Where in the grand scheme of things does this research fit?

## Slide 6: Approach
Task 1 Figure

## Slide 7: Approach
Restructure code in order to change storage formats, thereby enabling seamless linkage with other models
  Transition to a modern format, such as HDF5 and CSV, to create a reliable, robust storage system that can be easily validated
  Leverage existing software to allow harvesting into data catalog systems designed to service a broad range of users, enabling non-expert users to visualize model outputs, map model results, and compare with field data and with other models
  Consolidate input datasets into a single file system, allowing users to easily examine input parameters and boundary conditions
  Develop a utility to import previous W2 model inputs into the new data storage formats for the updated version
Task 2: Upgrade W2 Model Input and Output
Notes: Keep it simple and clear. Particularly with modeling efforts - the interaction of different models, modules and updates needs to be clear. Where in the grand scheme of things does this research fit?

## Slide 8: Approach
Task 2: Upgrade W2 Model Input and Output
    Excel utility to support develop input control files
Notes: Keep it simple and clear. Particularly with modeling efforts - the interaction of different models, modules and updates needs to be clear. Where in the grand scheme of things does this research fit?

## Slide 9: Approach
Develop a framework, using Python, to link CE-QUAL-W2 with modern scientific Python libraries, enabling development of new input/output and plotting analysis capabilities
  Develop plotting capabilities to visualize project bathymetry files, water quality and hydrodynamic time series, and 2D contour plots of reservoir water quality profiles
  Develop a prototype Jupyter notebook to link the capabilities together, to create a powerful and flexible self-documented user interface (UI) that is relatively simple to develop
  Update and extend this new interface throughout completion of subsequent tasks
Task 3: Create Python/Jupyter Model Framework
Notes: Keep it simple and clear. Particularly with modeling efforts - the interaction of different models, modules and updates needs to be clear. Where in the grand scheme of things does this research fit?

## Slide 10: Approach
Enable W2 to incorporate water quality and other environmental objectives into reservoir releases calculations, while balancing these with flood control, hydropower, navigation, water supply, and navigation objectives
  Incorporate capability into W2 to examine dam flow control impacts on downstream water quality and determine how downstream temperature and water quality objectives will be met
  Create capabilities in W2 to examine impacts of dams and flow regulation on downstream temperature and water quality conditions while identifying how operations may be improved to maximize ecosystem benefits
Task 4: Develop Reservoir Operations Capabilities
Notes: Keep it simple and clear. Particularly with modeling efforts - the interaction of different models, modules and updates needs to be clear. Where in the grand scheme of things does this research fit?

## Slide 11: Approach
Decouple water quality component from hydrodynamics in W2 in cases where the water quality state variable does not impact hydrodynamics, thereby increasing computational efficiency
  Run hydrodynamic simulations for a prescribed period, store output, and use data as input for multiple water quality simulations
  Implement a simultaneous equation solution of the water surface in all branches for the updated model, enhancing hydrodynamic stability of riverine segments
  Support increasing demand to include water quality operating objectives for water management by updating selective withdrawal algorithm to account for overlapping withdrawal zones for multiple outlets (versus simply adding them together)
  Evaluate using multi-core processing capability with numerical precision of simulations vs. fast code execution
Task 5: Upgrade Hydrodynamic & Water Quality Computation Engine
Notes: Keep it simple and clear. Particularly with modeling efforts - the interaction of different models, modules and updates needs to be clear. Where in the grand scheme of things does this research fit?

## Slide 12: Approach
Prepare and post final release version of CE-QUAL-W2 Version 5.0 to the ERDC website for release
  Conduct a case study demonstrating all capabilities included in the final release version of CE-QUAL-W2 and document in a technical note
  Post updated CE-QUAL-W2 Technical Reference Manual and User’s Manual to ERDC’s web site
  Prepare a final webinar using the case study and present to USACE District and Division staff, including water quality modelers and managers
Task 6- CE-QUAL-W2 v5.0 final version with documentation
Notes: Keep it simple and clear. Particularly with modeling efforts - the interaction of different models, modules and updates needs to be clear. Where in the grand scheme of things does this research fit?

## Slide 13: Field Engagement
Project Planning
  Team meetings & conference calls
  Periodic project updates to PDT, ERARG members, and field personnel by phone, web meeting, and email
Reporting
  Provided quarterly updates to the USACE Water Quality Committee
Field Work Coordination
  Coordination with NWD (Kathryn Tackley, Dan Turner, Alexis Mills, and Norm Buccola)

## Slide 14: Scheduled Products1
Scheduled Products |  |  | 
Description | Scheduled Due Date | Current Percent Complete | Projected Completion Date
 | (Qtr/Yr) | (%) | (Qtr/Yr)
1. CE-QUAL-W2 Version 4.5 | Q2/FY21 | 100 | Q2/FY21
2. CE-QUAL-W2 Version 5.0 Alpha | Q2/FY22 | 50 | Q2/FY22
3a. Python Framework 3b. Prototype Jupyter Notebook 3c. Plotting Capability | Q1/FY21 Q1/FY21 Q1/FY21 | 100 100 100 | Q1/FY21 Q1/FY21 Q1/FY21
4. CE-QUAL-W2 Operations Capability | Q2/FY22 | 50 | Q4/FY21
1 As per work unit documentation
Notes: Include all PRODUCTS/DELIVERABLES as specified in the original WU documentation

## Slide 15: Scheduled Products1
Scheduled Products |  |  | 
Description | Scheduled Due Date | Current Percent Complete | Projected Completion Date
 | (Qtr/Yr) | (%) | (Qtr/Yr)
5. CE-QUAL-W2 Version 5.0 Beta | Q2/FY23 | 0 | Q2/FY23
6a. CE-QUAL-W2 Version 5.0 Final 6b. User Manual 6c. Technical Reference Manual 6d. Webinar 6e. Technical Note | Q4/FY23 Q4/FY23 Q4/FY23 Q4/FY23 Q4/FY23 | 0 75 75 0 0 | Q4/FY23 Q4/FY23 Q4/FY23 Q4/FY23 Q4/FY23
1 As per work unit documentation
Notes: Include all PRODUCTS/DELIVERABLES as specified in the original WU documentation

## Slide 16: Additional Products/Achievements
Additional Products/Achievements | 
Description | (Qtr/Yr)
Recruited computer scientist at EL-EPW in FY21 New features presented at National Conference for Ecosystem Restoration (NCER), July 2021 Additional features developed for V4.5, funded by reimbursable projects New features presented at California Water and Environmental Modeling Forum (CWEMF), October 2021 | Q3/FY21 Q4/FY21 Q4/FY21 Q1/FY22

## Slide 17: FY21 Accomplishment 1: Extended CE-QUAL-W2 WQ Algorithms (Task 1)
General Constituents
Bacteria
CBOD
DGP, N2
TDG
Algae toxins
    H2S, CH4, SO4, Fe(II), FeOOH, Mn(II), MnO2
    Zero order
    First order
    Sediment diagenesis
Organic Carbon
Status: On Time

## Slide 18: FY21 Accomplishment 1: Full Organic Carbon Cycle and BOD (Task 1)
Status: On Time

## Slide 19: FY21 Accomplishment 1: Sediment Diagenesis Module (Task 1)
Inputs: csv format
Outputs: Bottom layer and averaged outputs
Simplified computations to steady-state
Add SOD and sediment fluxes for all water column layers
Add initial conditions for NO3 in sediment layers (layers 1 and 2)
Add an averaged SOD and sediment fluxes into the output for each segment
Add a subroutine for computing sediment POM and delete the corresponding parts in water-quality.f90
Add sediment POM (POC, PON and POP) computation (Subroutine SedimentPOM)
Add the correction for calculating SD_W12
Add a correction for PO4 partitioning coefficient in layer 1
Add partitioning of sediment NH4
Modify the numerical solution for CH4
Water Column
Active Sediment Layer
Deep Sediments
Surface cell
Bottom cell
Area
Status: On Time

## Slide 20: FY21 Accomplishment 2: Upgraded Model Input and Output (Task 2)
Added capability to use Excel to create the model control files
  Simplified editing of input files
  No graph.npt file required
  Easier cutting and pasting
  Simplified I/O
  Files more organized
  Variable names and explanations at user’s fingertips
  Formulae included in released Excel tool assist in control file development
Excel file w2_con.xlsm  w2_con.csv
Status: On Time

## Slide 21: FY 21 Accomplishment 3: Visualization Capabilities (Task 3)
Description: Visualization capabilities were developed for CE-QUAL-W2 using Python.
Plotting functions were developed for the meteorology and water quality input and output data.
Julian Days are converted to date-time format allowing the date axis to scale from minutes to decades with readable tick intervals and labels.
Default plot options were set to make clear and readable plots.
Status: On time
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 22: FY 21 Accomplishment 3: CE-QUAL-W2 Geometry QGIS Plug-in (Task 3)
Description: The CE-QUAL-W2 Geometry Preprocessor QGIS Plug-in allows fast and easy creation of model bathymetry files, given a digital elevation model (DEM) and a polyline shapefile of the centerline of the waterbody.
After loading the DEM and shapefile of the centerline, the tool generates the cross-sections.
The user can then split and/or merge cross-sections to refine the model bathymetry.
Then the model bathymetry can be exported for the CE-QUAL-W2 model.
Status: On time
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 23: FY 21 Accomplishment 3: CE-QUAL-W2 Geometry QGIS Plug-in (Task 3)
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 24: FY 21 Accomplishment 3: CE-QUAL-W2 Geometry QGIS Plug-in (Task 3)
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 25: FY 21 Accomplishment 3: CE-QUAL-W2 Geometry QGIS Plug-in (Task 3)
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 26: FY 21 Accomplishment 3: CE-QUAL-W2 Geometry QGIS Plug-in (Task 3)
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 27: FY 21 Accomplishment 3: CE-QUAL-W2 Geometry QGIS Plug-in (Task 3)
Split
Split
Merge
Split
Merge
Merge, then Split
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 28: FY 21 Accomplishment 4: WQ Operations Capability (Task 4)
Panel (a) and (b) are examples of optimal operation rules at a Corps dam (Folsom) that minimize flood risk while maximizing water supply given the evaluation of an ensemble of synthetic records.
Panels (c) and (d) are color coded to show how these various rules would have been applied during the historic record (e.g., blue = flood control release, red = hedge by releasing 80% of water supply demand).
  The black line shows what the reservoir storage would have been following these optimal rules.
  The grey line shows the observed reservoir storage during this period.
Status: On Time
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 29: FY 21 Accomplishment 4: WQ Operations Capability (Task 4)
Status: On Time
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 30: FY21 Accomplishment 5: Hydrodynamic Engine Updates (Task 5)
Added minimum water level (MINWL) above powerhouse as a criterion for moving to a different selective withdrawal structure
Added capability to set dynamic port elevation as active when a port selection rule is not active
Status: On Time

## Slide 31: FY 21 Accomplishment 6: CE-QUAL-W2 Version 4.5 Official Release
Description: CE-QUAL-W2 Version 4.5 has been completed and released. The executables, source code, user’s manual, and other documentation have been posted to ERDC’s GitHub and PSU’s website.
Updated algorithms
Updated and extensively edited user’s manual, five parts, 1,094 pages. Authors: Dr. Scott Wells and Dr. Zhonglong Zhang, Portland State University
https://github.com/EnvironmentalSystems/CE-QUAL-W2
http://www.ce.pdx.edu/w2/
Status: On time
Notes: Describe product and capability, importance/impact, etc.. Employ images generously. Tell a good story.

## Slide 32: Additional Features in Version 4.5 Total Dissolved Gas (TDG) (Funded by Portland District)
Estimates the forebay and tailwater TDG pressures resulting from reservoir operations.
TDG Computed from “N2+DO” and DGP
Status: On Time

## Slide 33: Additional Features in Version 4.5 Algae Toxins (Funded Oregon Clean Water Services)
CTP = fraction of algal group producing toxin
β = ratio of intra. toxin mass to mass of dry weight OM

## Slide 34: Additional Features in Version 4.5 Algae Vertical Migration (Funded by other organizations)
1D water column
No water velocity
Plankton velocity - time-varying velocity:
Source: NASA, https://climate.nasa.gov/blog/2788

## Slide 35: Additional Features in Version 5.0 Mercury (Hg) Cycle Module (Funded by Idaho Power Inc. and others)
Conceptual Mercury Cycle in a Water Body
Elemental Hg Inorganic Hg Methylmercury

## Slide 36: Synopsis
Funding
  FY20 $250K
  FY21 $385K
  FY22 $375K
  FY23 $290K
  Project $1300K
Project status
  On schedule
Project focus
  On target
Other comments
  PSU CESU needs to modified to fund FY22 development
Notes: Funding for all FY’s funded

## Slide 37: Summary
Updated and extended water quality algorithms
  Full Carbon cycle and BOD
  Sediment diagenesis module
  Total Dissolved Gas (TDG)
  Algae toxins
  Algae vertical migration
  Mercury cycle module
Upgraded model input and output
  CSV input and output, model control file
  Excel utility for input/output
Extended user interface
  Plotting capabilities
  CE-QUAL-W2 Geometry Preprocessor QGIS Plug-in
Water quality operations capability (to be integrated in V5.0)
Hydrodynamic engine updates (to be completed in V5.0)
Official V4.5 Release Completed