## Slide 1
The Corps Library for Environmental Analysis and Restoration of Watersheds (ClearWater): A New Integrated Multi-Dimensional Water Quality Modeling System
Todd Steissberg, PhD, PE
Environmental Laboratory
U.S. Army Engineer Research and Development Center (ERDC)
Co-Authors:
Isaac Mudge (USACE-MVN)
Kelsey Walak (USACE-SPK)
Anthony Aufdenkampe (LimnoTech)
Sarah Jordan (LimnoTech)
Jason Rutyna (LimnoTech)
Xavier Nogueira (LimnoTech)
Billy Johnson (LimnoTech
RD24
April 16, 2024

## Slide 2: Introduction: Nutrient Flow through Ecosystems
Nutrient flow through ecosystems has a profound impact on how species utilize resources across watershed scales.
  Primary production
  Species distribution and abundance
  Ecosystem productivity and stability
  Community composition and diversity
  Carbon sequestration
Human-caused disturbances are disrupting nutrient cycling, destabilizing ecosystem health and functioning.
Notes: Photo 1: Yellowstone National Park, showing complexity of landscape, flow, and vegetation
Photo 2: Complex and meandering flow across a landscape

## Slide 3: Introduction: Simulation of Nutrient Flow at Watershed Scales
Nutrient flow through ecosystems was not being simulated across watershed scales using a flexible integrated modeling system.
This hindered our ability to:
  Assess ecosystem risk analysis
  Predict morbidity and mortality of key species
  Predict spatial distribution of species across landscapes in response to changing conditions
  Identify effective ecosystem restoration strategies and management interventions
  Design measures to control the spread of invasive species
Notes: Photo 1: Terraced stream restoration project
Photo 2: River restoration, Trent River Valley, England

## Slide 4: Introduction: Objective
Water Resources Models
Water Quality Models (Nutrients & Temperature)
Ecological Models
Develop an integrated ecohydrology modeling system that simulates heat and nutrient flow through ecosystems.

## Slide 5: ClearWater: Next Generation Integrated Water Quality Modeling
ClearWater: Corps Library for Environmental Analysis and Restoration of Watersheds
Purpose: Link environmental models with existing water resources models that simulate runoff, rivers, and reservoir hydraulics and hydrology
ClearWater provides environmental simulation capabilities that are designed to leverage existing water resources models.
  The ClearWater water quality modules simulate constituent kinetics, heat budget processes, and vegetation growth cycles. Capabilities include:
    NSM: Nitrogen, phosphorus, and carbon cycling; dissolved oxygen, algae, etc.
    TSM: Temperature (heat budget)
    GSM: General Constituents
    CSM: Organic and inorganic contaminants
    MSM: Mercury
ClearWater contains legacy modules written in Fortran and C++ and next-generation modules written in Python (NSM and TSM)
  Engine computes the transport (advection and diffusion) of heat and constituent mass across the watershed
  Data visualization capabilities
  Framework to integrate multiple models.
Runoff
Reservoirs
Rivers

## Slide 6: ClearWater-Riverine
Clearwater-Riverine simulates temperature and advanced nutrient cycling in branching river systems and floodplains, incorporating hydrodynamic, water quality, and meteorologic inputs from multiple data sources and models.
  Flows: The model grid, volumetric flow, velocities, depths, diffusivity, etc. are provided by existing 2D water resources models.
    HEC-RAS (2D)
    GSSHA (in progress)
  Modules: Water quality kinetics and heat budget simulation capabilities in ClearWater-Riverine are furnished by ERDC's ClearWater modules (e.g., NSM).
  Transport: The ClearWater transport engine computes advection-diffusion of heat and mass through the model network.
  Framework: The ClearWater framework links all the components together and performs the water quality compute sequence.
Currently design is based on decoupled modeling, i.e., the flows are pre-computed by the hydro models.

## Slide 7: ClearWater-Riverine Example: E. Coli Transport in the Ohio River

## Slide 8: Modern Scientific Python
Built using the cloud-native geospatial Python stack being widely adopted by NOAA, USGS, NASA, etc.
An object-oriented architecture inspired by xarray-simlab / fastscape and CSDMS LandLab
Automated unit testing
https://numfocus.org/sponsored-projects
Notes: This [modern, cloud-native, geospatial Python] stack is designed to scale computations from a single set of values to multi-dimensional arrays, as shown in the icon for the xarray package, and scale from laptop to parallel computing to distributed cloud computing, powered by the Dask library that is built-in under-the-hood for xarray. All these libraries are very well supported by foundations, industry, and federal agencies.
We also wanted to follow modern numerical modeling coding patterns in widespread use by the geosciences community, so we we organized

## Slide 9: Model Coupling
Basic Model Interface (BMI)
  Provides a common set of functions
    To run models and exchange information and data on grids, variables, timesteps, etc.
  Shares data among models using a zero-copy approach
    Each model reads and writes to the same in-memory object using pointers
  Supports models written in C, C++, Fortran, Java, Python, Javascript, Julia
    NOTE: BMI must be implemented in the source code of a model before it can be used to couple that model to other BMI-compliant models
  Learn more: https://bmi.readthedocs.io
Modeling community moving toward systems of coupled models from modular model components.
BMI 2.0 has become the standard for model coupling

## Slide 10: Demo Case Study: Sumwere Creek — Domain & Mesh
Coarse Mesh Fine Mesh
Notes: Flow field is from HEC RAS-2D output in this case
Domain: 200 meters by 200 meters
Fictitious Topography/Bathymetry
  - Bathymetry bottom elevation constant at 20 m
  - Floodplain elevation constant at 24 m
  - Roadway elevation constant at 26 m
Two Unstructured Meshes Tested
  - Coarse Mesh: Base Mesh of 10 m by 10 m
  - Fine Mesh: Base Mesh of 4 m by 4 m with a 2 m by 2 m refinement within the creek

## Slide 11: Demo Case Study: Sumwere Creek — Domain, Mesh, and Hydrodynamic Boundary Conditions
Coarse Mesh Fine Mesh
Upstream: 3 cms
Spring:
1 cms
Powerplant:
0.5 cms
Downstream:
20.75 m
Notes: HEC-RAS Boundary Conditions
  - Upstream Flow for Sumwere Creek constant at 3 cms (1st hour ramping from zero)
  - Downstream Stage for Sumwere Creek constant at 20.75 m
  - Flow for Cold Spring Creek constant at 1 cms (1st hour ramping from zero)
  - Flow for Power Plant Chute constant at 0.5 cms (1st hour ramping from zero)

## Slide 12: Demo Case Study: Sumwere Creek — Depth at End of Simulation
Notes: Profile of the coarse and fine mesh depth results along the magenta line in the plan view plot.
This shows the depth at the upstream boundary at 1.27 m and 1.23 for the coarse and fine mesh, respectively (4 cm difference); these depth difference are due to mesh resolution. This shows approximately 0.5 m of hydraulic head is required to overcome the bed friction for this flow rate. A uniform Manning’s roughness coefficient of 0.06 was used in both meshes.

## Slide 13: Demo Case Study: Sumwere Creek — Velocity at End of Simulation
Coarse Mesh Fine Mesh
Notes: Differences in velocities between the meshes are due to varying spatial resolution in each mesh

## Slide 14: Demo Case Study: Sumwere Creek — Temperature Boundary Conditions
Coarse Mesh Fine Mesh
Upstream: 15˚C
Spring:
5˚C
Powerplant:
20-25 ˚C
Notes: Boundary conditions are the same for both the coarse and the fine mesh.
Designed to show longitudinal mixing across the river
Exploration of different extremes (cool water from spring-fed tributary versus warm water from powerplant)

## Slide 15: Demo Case Study: Sumwere Creek — Temperature Boundary Timeseries
Coarse Mesh
Upstream: 15˚C
Spring:
5˚C
Powerplant:
20-25 ˚C
Notes: Timeseries of boundary conditions (stable, except for powerplant discharge)
Powerplant discharge has two peaks during the day (one in the morning, one in the afternoon)

## Slide 16: Demo Case Study: Sumwere Creek — Meteorological Timeseries
Notes: Meteorological timeseries used as inputs to TSM.
Air temperature and solar heat flux both peak during the day and drop at night.
Timeseries from Arizona (extreme cycles to help capture impact of TSM).

## Slide 17: Results – Animation
Coarse Mesh Fine Mesh
Notes: You can see the mixing.
Ultimately reaches steady state.

## Slide 18: Results – Warm Powerplant Inflows
Coarse Mesh Fine Mesh
Notes: Pulses from powerplant.
Can see a lot more transverse mixing from the powerplant and spring in the fine mesh compared to the coarse mesh.
Can see more detail on the plume of warm water.
This all shows transport very clearly, but what about our energy budget model / TSM?

## Slide 19: ClearWater Framework Summary
ClearWater’s Python-based framework allows easy integration with powerful interactive visualization packages
  Enhanced understanding of complex environmental/ecological outcomes
  Iterative analysis and scenario discovery
  Multidimensional exploration across time and space
  Effective communication of results across teams and stakeholders
Notes: Building on the shoulders of giants.
We do not build or maintain any of these libraries.

## Slide 20: Benefits
Model linking using BMI enables a seamless exchange of data and information between different components of the integrated modeling system.
Facilitates data-driven decision-making
Enhances collaboration between scientific disciplines
Integrated models that simulate the interactions between heat, nutrients, water flow, and vegetation enable a comprehensive representation of ecosystem dynamics.
  Accurate representation of real-world processes
Enables assessment of the ecological responses to various environmental changes, such as land use modifications, climate change, or nature-based feature design and Best Management Practices (BMPs)
Example applications:
  Setting nutrient loading limits
  Designing buffer zones
  Implementing BMPs to restore aquatic ecosystems

## Slide 21: Questions?